## Slide 1: Physical Layer for a Quantum Communication Channel with Discrete Variables
Quantum Mining Meeting
17th May 2019
Mariana Ferreira Ramos

## Slide 2: Quantum Physical Layer with discrete variables
QTx
QTxBasis
QTxBits
ModeSelection
ModeSelection
DataOut
QRxBasis
DVQuantum_TxRx
QRx
QChannel
QBER UB
Bit synchronism.
Mode synchronism.
Polarization compensation.
HOW?
Emulator in netXpto simulator.
2 FPGA’s (1 for QTx and 1 for QRx).

## Slide 3: Quantum Physical Layer
Quantum Communication Channel
4 Possible Polarization States.
2 Non-orthogonal basis.
Bit ‘0’ and ‘1’.
2 Possible measurement basis.
Diagonal and Linear.
QTx
QRx
Attenuation depends on the optical fiber length.
Polarization random drift which depends on the birefringence of the optical fiber.

## Slide 4: Quantum Physical Layer Polarization Basis Aligment
Quantum Communication Channel
Polarization Basis Alignment Algorithm
EPC
Feedback signal
Measurements

## Slide 5: Quantum Physical Layer Polarization Basis Aligment
0
1

## Slide 6: Quantum Physical Layer Polarization Basis Aligment
Transmission window of 1 ms under heavy external conditions.
QBER estimation sliding window of 1 ms.
1 qubit in each 100 transmitted qubits to polarization control.
Switch to actuation mode as soon as the QBER rises a 2% boundary below the 3% user-defined threshold.
Data qubits with 0.1 photons in average.
Control qubits with an amplitude high enough to guarantee that at least 1 photon reaches the receiver.

## Slide 7: Quantum Physical Layer Polarization Basis Aligment
Data transmission is interrupted during algorithm’s actuation mode.
Overhead below 1.5%.
Average channel QBER below 1%.
Maximum QBER of 2.1% during data transmission.

## Slide 8: Quantum Physical Layer
Quantum Communication Channel
Polarization Basis Alignment Algorithm
EPC
Feedback signal
Measurements
QTx
QRx
QChannel
QTxBasis
QTxBits
ModeSelection
ModeSelection
DataOut
QRxBasis
DVQuantum_TxRx
Full Quantum Physical Layer for discrete variables transmission using Polarization Encoding.
QBER UB

## Slide 9: Outputs
M. F. Ramos, N. A. Silva, N. J. Muga, and A. N. Pinto, “Algorithm for compensation random drifts in polarization encoding quantum communications,” submitted for journal publication, March 2019.
Armando N. Pinto, Mariana F. Ramos, Andoni C. Santos, Nuno A. Silva, and Nelson J. Muga, “The Impact of Fiber Random Birefringence in Polarization-Encoded Quantum Communications”, submitted for conference publication, April 2019.
M. F. Ramos, N. A. Silva, N. J. Muga, and A. N. Pinto, “Fast Polarization Basis Alignment For Quantum Communications,” submitted for conference publication, May 2019.