## Slide 1: Quantum Communication Channel using Discrete Variables
Quantum Mining Meeting
17th May 2019
Nuno A. Silva
Mariana F. Ramos
Nelson J. Muga

## Slide 2: Quantum Physical Layer with discrete variables
QTx
QRx
QChannel
ALICE
BOB
Quantum communication channel using discrete variables to encode information.
Alice is able to encode 4 states of polarization using 2 non-orthogonal bases.
Bob is able to choose one out of two bases to perform the measurements.
10 km of uni-directional quantum channel.

## Slide 3
MZ modulator
Filter
EPC
VOA
WDM
AWG
MZ modulator
FIBER
ALICE
EPC controller

## Slide 4
ALICE
One of the 4 states of polarization is randomly chosen.
Polarization encoding is performed using an electronic polarization controller, using 4 values of voltage (1 for each waveplate).
Additional synchronism signal in a different wavelength.
Quantum signal is pulsed using a MZM modulator in order to obtain in average 0.1 photons per pulse.
Both quantum and synchronism signals are coupled using a wavelength multiplexer.

## Slide 5
BOB
FIBER
WDM
Filter
PIN
EPC
PBS3
EPC controller
Trigger
Data Out
Data Out
Trigger

## Slide 6
BOB
Bob chooses one of two possible bases to measure single photons.
Two single-photon detectors: one to measure bit ‘0’ and other to measure bit ‘1’.
Quantum and synchronism signals are splitted using a wavelength multiplexer.
Data is processed by the EPC controller unit.
Synchronism is guaranteed using the additional signal sent by Alice.